## Slide 1
TDPS Oral Presentation
Han Liu
Cheng Yang
Chengwei Wang
Rui Cao
Team No.29
Yangchen Yu
Songjiang Lai
Yutong Song
Hongfei Wu

## Slide 2
CONTENTS
1
Hardware Design
2
Line Tracing
3
Bridge Crossing
4
Color Matching
5
6
Navigation in Patio 2
7
Item Releasing
Wireless Communication
8
Question & Answer

## Slide 3
01
Hardware Design
Speaker: Cheng Yang

## Slide 4
12v battery
Raspberry pi
L298N and L298P
Camera for line tracing and color recognition
Wheels with radius of 40mm
motor
HC-12 with USB TTL for communication
Navigation module for patio 2
Ejection Device
mbed
Hardware Connection Diagram
Elements:

## Slide 5
Raspberry Pi 3B
Battery
5V
Regulator
Battery
12V
Geomagnetic module AND
DWM 1000
Mbed Lpc1768
HC-12
HC-12
USB TTL
Computer
Driver
Motor1
Motor2
Motor3
Motor4
Steering engine
PWM
TXD
RXD
Camera
Hardware system
:
Design Graphic

## Slide 6
Bill List
 | Component | Type | Unit Price(CYN) | Quantity | Costs (CYN)
1 | Driver | L298N | 6 | 2 | 12
2 | Raspberry Pi | 3B | 200 | 1 | 200
3 | Camera | S329 | 65 | 1 | 65
4 | Gyroscope Sense | GY88 | 68 | 1 | 68
5 | Micro Servo | SG90 | 12 | 2 | 24
6 | Wireless Module | HC-12 | 20 | 2 | 40
7 | UWB | DWM1000 | 150 | 2 | 300
8 | Supporting plate and screw package With PCB |  | 170 | 1 | 
Budget |  | 1000 CYN |  | Total cost | 879

## Slide 7
02
Line Tracing
Speaker: Han Liu

## Slide 8
Overview
1
2
1
2
Part 1
Image Processing
Part 2
Motor Control
Color discrimination
Coarse-grained discrimination
Calculate central coordinates
Forward Direction Correction

## Slide 9
Color Discrimination
Capture Frame by Camera
Filter Frame by
Gaussian Blur
Crop Frame to the Proper Size
Find Road Center
Motor Control
Edge Detection
End
Begin

## Slide 10
Gaussian Blur
Original Image
Blur Image
Formula:
Advantage:
Remove high-frequency noise pollution while retaining most of the original image
The two-dimensional Gauss function has rotational symmetry, the smoothness of the filter is the same in all directions
A relatively small amount of computation

## Slide 11
Binarize With Different Threshold Threshold
H: [10,30]
S: [15,60]
V: [120,200]
H: [10,30]
S: [15,60]
V: [120,200]
H: [16,20]
S: [25,45]
V: [160,190]

## Slide 12
Dilate Process
Kernel Size :
Kernel Size :
Kernel Size : 7

## Slide 13
Coarse-grained Discrimination
Coarse
Smooth
Smooth

## Slide 14
Motor Control

## Slide 15
Motor Control
0.25
0.50
0.75

## Slide 16
Motor Control
Image Center
Path Center
Turn Right！

## Slide 17
03
Color Matching
Speaker: Chengwei Wang

## Slide 18
Procedures
Color Recognition:
Recognize the color in the identification point
Color Tracking
Track the object according to recognized color
Move to the identification point
Move to the colored square at the right-hand side of the diamond

## Slide 19
Color Recognition
1
2
3
HSV Color Dictionary Measure the HSV value of the desired color，then define the HSV Color Dictionary
4
Image Binarization Make the entire image look bright black and white
Convert RGB to HSV HSV model is more in line with the way of describing and explaining colors, more natural and intuitive
Remove The Background Color Background will be chaotic, so we have to remove background color
5
6
Filter Color Components
We get different image by filtering the frames captured by the camera with different color components
Recognize The Color Calculate the area of the white area, the largest is the color of the object

## Slide 20
Color Tracking
blue
purple
green
Record HSV value of recognized color
Convert frame to HSV with HSV recorded value to find the color
Make sure center of the color is found
Turn left
left
Capture frame by camera
Compare with center of frame
right
intermediate
Turn right
Go straight
If color area is more than 450000
Yes
Stop
No

## Slide 21
04
Bridge Crossing
Speaker: Yutong Song

## Slide 22
Bridge Crossing
Task goal
Find the bridge, cross it
The car can't walk straight on a bridge
Find the gate, go through it, then stop
Route can’t exceed specified location

## Slide 23
Bridge Crossing
Corresponding solution:
Receive the signal at this position:
Get Color information
Information processing
Go straight on the bridge:
Adjust direction
Center coincidence

## Slide 24
Bridge Crossing
IF color1 in THEN
DO Bridge crossing；
DO turn right;
IF center correct THEN
DO go straight;
ELSE keep turning
END IF
ELSEIF color2 in THEN
DO Gate crossing；
ELSE line tracing;
END IF
Receive the signal
at the position
Go straight on the bridge

## Slide 25
Bridge Crossing
Go straight
Color in
Turn right
Change the direction
Center coincidence

## Slide 26
05
Navigation In
Patio 2
Speaker: Hongfei Wu
Yangchen Yu

## Slide 27
TW-TOF (two way-time of flight)
- -
Overview
1
2
3
Fixed beacon position, label and detect key point coordinates
Beacon gives real-time position to vehicle through the distance given by the beacon
and direction given by the geomagnetic module
The car corrects its direction according to the current position and the coordinates of the key point until it reaches the key point.
4
The car starts to correct its position according to the next key point and repeats the above process until it reaches the end point.

## Slide 28
Path Planning
Sampling key point coordinates at each corner
Sampling key point coordinates at intervals of 5 meters for straight-line Paths

## Slide 29
UWB Additional Information
TW-TOF,two way-time of flight
TOA
TDOA
TOF time of flight
UWB channal
UWB standard worldwide

## Slide 30
TW-TOF: two way-time of flight
TOA
TDOA
TOF: time of flight
UWB Channel
UWB Additional Information

## Slide 31
- - （TWTOF）
Our software is object-oriented and has a clear structure based on the following tasks:
Operating the DW1000 chip via SPI
Performing a two-way ranging scheme and transmitting the acquired distance
Structure of software
UWB Overall Structure
Coordinate Transformation (TDOA)

## Slide 32
PCB craft：FR-4 Power supply interface：micro-USB (5.0V) / pin SWD interface：Yes (available with ST-Link downloader) Output Interface：UART4, USB virtual serial port main controller：STM32F105RCT6 (64pin External crystal：Passive 12Mhz crystal PCB ruler：Length 24mm* width 35mm
PCB design

## Slide 33
06
Item Releasing
Speaker: Rui Cao

## Slide 34
Item Releasing
Nam
1
2
Aim
Release the item into the lake or box
Consideration
The size of the fence
Environmental Impact of Throwing Objects
Cost

## Slide 35
3
Idea 1 (abandoned at the beginning)
1. Easy to control
2. Suitable for the mission
1. High cost, beyond budget
2. There is more easier way
3. Need expertise, laborious and time-consuming
Advantages
Abandoned reasons
Robotic Arm

## Slide 36
Ejected device
The internal motor of the device compresses the spring through the gear to generate elastic force and shoot the object.
1.High voltage
2.Huge and heavy
Raspberry Pi as switch
L298N or mbed as switch
Can not provide enough voltage
Strong recoil
Principle
Difficulties
Solutions
Abandoned reason
3
Idea 2 (abandoned at the tests)

## Slide 37
Acrylic tube, rubber band, motor, small wooden stick, line
Elastic force of the rubber band to release item
Low cost
Lower voltage requirements
Easy to build and control
Materials
Principle
Disadvantages
Adopted reason
3
Idea 3 (adopted)
DIY simple luncher
Difficult to tighten the rubber band
Easy to get stuck

## Slide 38
1
3
5
2
4
Power on the motor
Pull thin wire
Pull out stick
Eject object
Connect motor with stick
Fix the pipe
Fixed motor position

## Slide 39
4
The choice of item
item
Ping pang ball
reasons
1.Cheap, can reuse
2.No pollution, can salvaged
3.Light weight.
4. Easy to shoot with rubber bands

## Slide 40
07
Wireless communication
Speaker: Songjiang Lai

## Slide 41: Wireless communication
Generally speaking, raspberry pi sent for interface is divided into hardware serial port and mini serial port. We will swap the raspberry PI hardware serial port with the mini serial port default mapping.
Specific steps:
Raspberry pie environment debugging
Code input
PC sends data
PC receives data

## Slide 42: Raspberry PI serial communication Settings
Lorem ipsum dolor sit amet, consectetur adipiscing elit. Sed imperdiet tincidunt velit laoreet facilisis.
Lorem ipsum dolor sit amet, consectetur adipiscing elit. Sed imperdiet tincidunt velit laoreet facilisis.
Download pi3 miniuart-bt overlay.
Edit the config.
Edit /boot, delete serial1,115200
Turn off onboard bluetooth
Edit "ttyAMA0" to "ttyS0"
Update and restart
Connect
Mini serial port for setting.
Over.

## Slide 43: HC-12 models and principles
Design Graphic
Web Coding
Enviromental
The information
PC received
TXD
TXD
Raspberry
Pi
RXD
RXD
TXD
computer
RXD
Pieces of code:
Information includes student names, student numbers, current time (system time), team number.

## Slide 44
08
Question & Answer
THANK YOU!

## Slide 45
08
Question & Answer